## Slide 1: Spatial Attention EEG Experiment Manual
Akira Takeuchi
ver. 07/01/2024

## Slide 2: -> Examine the listeners’ response against spatially Masked speech (Spatial Attention) #Speech Recognition Threshold (SRT) task #use CRM corpus #EEG measurement Scripts are available at: https://github.com/50516021/DSI24tutorial/tree/main/SpatialAttention_exp
Purpose

## Slide 3: Studio setting
picture from:
https://www.nhk.or.jp/strl/english/publica/bt/64/6.html
・use FL, FR, and BC in 22.2ch
・ L/R has 45 degrees from the center line

## Slide 4: Requirements [Hardware]
PC with MATLAB
Windows PC with DSI-Streamer
-> They can be one PC, but better to be separated
Audio Interface
Audio cables
iPad with TouchOSC mk1 app
3 Loudspeakers
A network can be shared
between the PC and iPad

## Slide 5: Requirements [Hardware: DSI-24 set]
MMBT Trigger generator
DSI-24
Trigger cable
MMBT USB cable
Wireless receiver
Trigger hub
Trigger hub power cable
Wireless repeater
BT dongle
DSI-streamer PC
MATLAB PC

## Slide 6: Location (channel) setting
target :L
masker :
・co-located -> L
・separated (same side) -> R
・separated (opposite side) -> BC (Back Center)
→most practical situation
investigate SNR threshold which can make differences between each channel configuration
L
R
BC

## Slide 7
PC2 (Windows)
DSI streamer
DSI-24 System Diagram
DSI-24
Wireless
repeater
Wireless
Trigger Hub
PC1 (Mac)
MATLAB
Sound
Audio interface
EEG & Trigger
Trigger
Sound
Speaker
Wireless receiver
Trigger
EEG & Trigger
  Recording on EDF/CSV file
  Can be set in separate spaces without a wired connection
Wireless
Repeater

## Slide 8: Requirements [Software]
[Recording PC]
DSI-Streamer
Blue Tooth Driver
[Experiment PC]
MATLAB
cloned scripts from GitHub repo
[iPad]
TouchOSC mk1
load the template ‘SpatialAttention.touchosc’

## Slide 9: Preparation - Sound Calibration
① Connect the Audio Interface to the Speakers
② Connect the Audio Interface before starting MATLAB
③ Test the Volume with ‘Soundtest.m’ and tune all the speakers for 57 dB at the listening point
(masker sound is tuned to be 70 dB SPL with this calibration)

## Slide 10: Preparation - Network
① Make sure that the laptop and the
iPad are connected to the same Wi-Fi
② Open Matlab on the laptop
③ Open TouchOSC on the iPad
④ Make sure your IP address and
port numbers on both MATLAB codes
and touch OSC
⑤ run ‘OscConnectionTest.m’ and make sure the connection between the PC and iPad
PC address
iPad address

## Slide 11: Preparation - Trigger
① Make sure the trigger receiver is fully charged and inserted into DSI-24
② run ‘makeTrigertest_BDF.m’
④ Make sure the triggers appear in the DSI-streamer screen

## Slide 12
Run [Variables ①]
- SpAt_main.m -
check:
・port number (iPad as well)

## Slide 13
Running [Variables ②]
- +data_load/makestimuluslist.m -
(function script)
check:
・[sn]
the value of all SNR you want to try
・[numSph]
number of trials of each condition
・[StartRange]
variation of the start time of target sound

## Slide 14
Running [procedure]
① Make sure every variable
② Run ‘SpAt_main.m’
③ Enter the participant’s name into a popup window
- Do not include ‘_’ in the participant’s name
④ Press any button on the iPad and start the experiment

## Slide 15: DSI-24 - Comfortability
  Doesn’t require gel, so…
  Participants can easily manage schedules
  (don’t need to care about their hair)
  The position can be easily changed
  Can be used wireless, so…
  Can pause the experiment and take breaks
  Flexible, stress-free movement

## Slide 16: DSI-24 - Robustness
  Each electrode has an independent amplifier, so…
  robust to an external electric field
  Entire the structure can fit and hold the participant’s head
  robust to movement
  stable position

## Slide 17: DSI-24 - Setup & Care
  Has one touch nob and an independent top piece
  can be easily and quickly set
  The headset can be cleaned with the brash with sanitizer
  reduce the time for care
  several experiment sessions in a day